The KA9Q-radio Package
2022 Dayton Hamvention
21 May 2022
Phil Karn, KA9Q
karn@ka9q.net

---
Basics
- Receive only, for now
- Fast convolution for efficient multichannel downconversion
  - How far can I go without a FPGA? (pretty far!)
- IP multicast for data and control/status
  - Standard VoIP protocols for data: RTP/UDP/IP
  - Custom TLV-based UDP protocol for control/status
    - Binary, compact, extensible

---
airspyd/airspyhfd/funcubed/hackrfd
iqrecord
Control
radiod
opusd
pcmrecord
packetd
Stereod
monitor
aprsfeed
aprs
rotors
aprs-is

---
Time domain
Forward FFT
Frequency domain
X
Filter response
Response must be windowed to limit impulse response
Freq domain
Inverse FFT
Output is automatically downsampled by ratio of block sizes
Time domain

---
0 1 2 3
Overlap sets maximum duration of filter impulse response
6 7 8 9
X 1 2 3
Forward transform, multiply by filter response, inverse transform
X 4 5 6
X 7 8 9
3 4 5 6

---
Test uses
- Turnkey APRS i-Gate
  - Funcube Pro+ dongle & RPi3
- Ham VHF/UHF FM vacuum cleaner
  - Every FM channel on 2m, 125cm and 70cm with three Airspy R2s (~9 MHz each)
  - One Airspy R2 per RPi 4; 60% CPU idle
  - Also decodes and reports APRS
- HF general coverage receiver
  - AirspyHF & RPi 4
  - “parasitic” WSPR decoding

---
To do
- More front ends
- Power spectrum pseudo-slices
- Discovery and autoconfiguration
  - Use IETF Zeroconf
- User interfaces
  - How should a radio work?
- Demodulators for DMR, D*Star, etc
  - Packet and WSPR done
- Documentation!

---
Fast convolution observations
- Elegant and efficient, but devil in details
  - FIR length <= forward FFT overlap
  - Coarse tuning in increments of 1/block duration
  - Fine tuning with arbitrary resolution
- Heavy lifting done by FFTW3
  - Very widely used, heavily tuned for many CPUs
  - Forward FFT is shared by all slices
- FFT and IFFTs in separate threads

---
Multicast conclusions
- Multicast is very flexible and elegant, but:
  - Only practical within a LAN
  - Cheap switches and WiFi base stations have gotchas
  - An isolated dumb switch can work fine; just keep total load less than slowest port speed

---
- Source:
  - http://github.com/ka9q/ka9q-radio